## Slide 1
Example:
Assume battery capacity is 25 Ah
Assume a fully discharged cell
Charge the battery at current for 4 hours, the total will add to: 2A*4h = 8Ah
State of charge of the battery at the end of charging cycle (Coulomb-Counting):
BATTERY CHARGING: BATTERY STATE OF CHARGE (%)
Notes: The battery SOC can be calculated using a technique known as coulomb counting or current integration. Let’s look at a simple example, Assume battery capacity is 25 Ah and assume a fully discharged cell. If we charge the battery at 2𝐴 current for 4 hours, the total accumulated Amp hours will add to: 2A*4h = 8Ah.
Therefore (Visual 3), the Battery State of charge the end of charging cycle using Coulomb-Counting is 32%:
𝑆𝑂𝐶= (𝑇𝑜𝑡𝑎𝑙 𝐶ℎ𝑎𝑟𝑔𝑒 𝐼𝑛𝑝𝑢𝑡)/(𝑀𝑎𝑥𝑖𝑚𝑢𝑚 𝐶𝑒𝑙𝑙 𝐶𝑎𝑝𝑎𝑐𝑖𝑡𝑦)=(8 𝐴ℎ)/(25 𝐴ℎ)=32%

## Slide 2
BATTERY CHARGING: TIME DOMAIN
This method is a traditional method used for SOC calculation
The method is also known as book keeping, current integration is performed and is compared to the nominal battery capacity thus SOC can be calculated
  is the battery nominal capacity
  is the cell state of charge
  is the instantaneous cell current
  Sign convention: for discharge, for charge
  is the time.
  : Coulomb efficiency
Notes: What we just did in this example is that we added up or “integrated” the current going into the battery in a specific period of time and then divided by the total capacity. Therefore the Coulomb counting equation can be written as follows:
Where, the battery state of charge at time t is equal to the battery initial state of charge indicated by SOC at time zero and then subtracted from the integral of the current from time zero to time t and then finally divided by the battery capacity indicated by the term “Cn”.
One note to consider is that current sign convention is positive when the battery is discharged and negative when the battery is charged. Therefore, the battery state of charge increase when the current is negative because the integral term becomes positive and decreases when the current is positive because the term becomes negative.
What we just did in this example is that we added up or “integrated” the current going into the battery in a specific period of time and then divided by the total capacity. Therefore the Coulomb counting equation can be written as follows (Visual 4):
𝑆𝑂𝐶(𝑡)=𝑆𝑂𝐶(0)−1/𝐶_𝑛 ∫_0^𝑡▒〖𝑖(𝜏)𝑑𝜏〗
Where (Visual 5), the battery state of charge at time t is equal to the battery initial state of charge indicated by SOC at time zero and then subtracted from the integral of the current from time zero to time t and then finally divided by the battery capacity indicated by the term “Cn”.
One note to consider is that current sign convention is positive when the battery is discharged and negative when the battery is charged. Therefore, the battery state of charge increase when the current is negative because the integral term becomes positive and decreases when the current is positive because the term becomes negative.

## Slide 3
Advantages:
The main advantage of coulomb counting is that it is simple to be implemented
It can be applied to all battery chemistries
Disadvantages:
Requires regular need for calibration since error accumulation occurs (due to sensor noise and inaccuracies) over time due to integration.
A complete charge and discharge has to be conducted which limits its practical applications
Requires an accurate initial SOC in order to provide an acceptable accuracy
Additional information such as cell temperature, charge/discharge efficiency, and capacity degradation due to cycling can enhance the accuracy of the coulomb counting technique
BATTERY CHARGING: ADVANTAGES/DISADV.
Notes: The main advantage of coulomb counting is that it is simple to be implemented and can be applied to all battery chemistries
- However, the technique requires regular need for calibration since error accumulation occurs (due to sensor noise and inaccuracies) over time due to integration.
And it requires an accurate initial SOC in order to provide an acceptable accuracy
In addition, additional information such as cell temperature, charge/discharge efficiency, and capacity degradation due to cycling can enhance the accuracy of the coulomb counting technique

## Slide 4
Integration of the function represents the area under the curve
BATTERY CHARGING: DISCRETE TIME DOMAIN
http://www.mathcs.emory.edu/~cheung/Courses/170/Syllabus/07/rectangle-method.html
Notes: - Let’s review two basic concepts, (1) A discrete-time sequence {} may be generated by periodically sampling a continuous-time signal at uniform intervals of time.
- The spacing between two consecutive samples is called the sampling interval or sampling period
- The Reciprocal of sampling interval , denoted as , is called the sampling frequency:
As you sample at a higher sampling frequency, you are capturing more samples and you are increasing the accuracy of the signal.
The second concept is if you have a continuous function f(x), by Integration of the function you are calculating the area under the curve.
In BMS, as we calculate the SOC using coulomb counting, you are integrating the current, so you are essentially calculating the area under the curve as shown in the figure. Every time you take a current sample, you multiply the current by the sampling interval DetlaT and sum it up to the total Ah accumulated to this moment and that’s how you update the battery SOC.
- Let’s review two basic concepts, (1) A discrete-time sequence {𝑥[𝑘]} may be generated by periodically sampling a continuous-time signal at uniform intervals of time.
- The spacing 𝑇_𝑠 between two consecutive samples is called the sampling interval or sampling period
- The Reciprocal of sampling interval 𝑇_𝑠, denoted as 𝐹, is called the sampling frequency:
𝐹=1/𝑇_𝑠
As you sample at a higher sampling frequency, you are capturing more samples and you are increasing the accuracy of the signal.
The second concept is if you have a continuous function f(x), by Integration of the function 𝑓(𝑥), you are calculating the area under the curve.
In BMS, as we calculate the SOC using coulomb counting, you are integrating the current, so you are essentially calculating the area under the curve as shown in the figure. Every time you take a current sample, you multiply the current by the sampling interval DetlaT and sum it up to the total Ah accumulated to this moment and that’s how you update the battery SOC.

## Slide 5
OCV-R Battery Model
SIMPLE MODEL (OCV-R)
Notes: - The simple battery model is as shown in the figure, the voltage source represents the OCV which is function of the battery state of charge. Then, the battery charging and discharging internal resistance are reprensted as RChg and Rdis. By subtracting the voltage drop across the resistance from the battery OCV, you can calculate the battery terminal voltage V.
The battery internal resistance is function of the battery temperature, SOC and life.
- In the following section, we are going to simulate the simple battery model using MATLAB and Simulink.

## Slide 6
BATTERY MODEL